## Slide 1: Combinational Logic II Optimization
CSCI 2050U - Computer Architecture
Randy J. Fortier
@randy_fortier

## Slide 2: Outline
Optimization
  Algebraic simplification
  Karnaugh maps
Common components

## Slide 3: Optimization
CSCI 2050U - Computer Architecture

## Slide 4: Boolean Algebraic Simplification
Boolean algebraic simplification is one way to optimize a circuit
  Simplification involves using a set of axioms/logical equivalences to eliminate operators, or even variables from an expression
  A smaller expression normally translates to a simpler/cheaper circuit
  The resulting expression must be logically equivalent

## Slide 5: Boolean Algebraic Simplification
Some axioms are intuitive:
AND Form | OR Form | Name
1x = x | 0 + x = x | Identity law
0x = 0 | 1 + x = 1 | Null law
xx = x | x + x = x | Idempotent law
xx’ = 0 | x + x’ = 1 | Inverse law

## Slide 6: Boolean Algebraic Simplification
Some axioms are intuitive:
AND Form | Name
x’’ = x | Double complement law

## Slide 7: Boolean Algebraic Simplification
Other axioms are familiar from (non-Boolean) algebra:
AND Form | OR Form | Name
xy = yx | x + y = y + x | Commutative law
(xy)z = x(yz) | (x + y) + z = x + (y + z) | Associative law
x + yz = (x + y)(x + z) | x(y + z) = xy + xz | Distributive law
Notes: Note the bottom left example is not exactly the same as non-Boolean algebra, but makes sense if you think about it.

## Slide 8: Boolean Algebraic Simplification
Others have been proved by Mathematicians:
AND Form | OR Form | Name
x(x + y) = x | x + xy = x | Absorption law
(xy)’ = x’ + y’ | (x + y)’ = x’y’ | DeMorgan’s law

## Slide 9: Boolean Algebraic Simplification
Let’s do an example:
f(x,y,z) = xy + x’z + yz
= xy + x’z + yz1 (identity)
= xy + x’z + yz(x + x’) (inverse)
= xy + x’z + yzx + yzx’ (distributive)
= xy + x’z + x(yz) + x’(yz) (commutative x2)
= xy + x’z + (xy)z + (x’z)y (associative x2)
= xy + (xy)z + x’z + (x’z)y (commutative)
= xy(1 + z) + x’z(1 + y) (distributive x2)
= xy1 + x’z1 (null x2)
= xy + x’z (identity x2)

## Slide 10: Boolean Algebraic Simplification
Let’s do another example (our Neg expression from earlier):
f(x,y,z) = xy’z’ + xy’z + xyz’ + xyz
= xy’(z’+z) + xy(z’+z) (distributive x 2)
= xy’1 + xy1 (inverse x 2)
= xy’ + xy (identity x 2)
= x(y’+y) (distributive)
= x1 (inverse)
= x (identity)
Notes: f(x,y,z) = xy’z’ + xy’z + xyz’ + xyz
= xy’(z’ + z) + xy(z’ + z) (distributive)
= xy’1 + xy1 (inverse)
= xy’ + xy (identity)
= x(y’ + y) (distributive)
= x1 (inverse)
= x (identity)

## Slide 11: Boolean Algebraic Simplification
The main problem with Boolean algebraic simplification is that it is not obvious what to do next
  We need an oracle to tell us which axiom to use next
  This is not a algorithmic approach
  We need something systematic, so we can never fail if we follow the steps

## Slide 12: Karnaugh Maps (K-Maps)
A K-map is a systematic way of simplifying Boolean algebraic expressions (in SOP form; alternatively truth tables)
  First, we draw a sort of coiled-up truth table:
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 13: Karnaugh Maps (K-Maps)
Next, we look for rectangles that are made entirely of 1s
  We look only for rectangles that are size 2n (for any n)
  We prefer rectangles that are larger over smaller rectangles
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 14: Karnaugh Maps (K-Maps)
Next, we look for rectangles that are made entirely of 1s
  This K-map has 4 spots
  Does it have any rectangles of size 4? (e.g. 2x2)
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 15: Karnaugh Maps (K-Maps)
Next, we look for rectangles that are made entirely of 1s
  This K-map has 4 spots
  Does it have any rectangles of size 4? (e.g. 2x2) No (there is only one)
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 16: Karnaugh Maps (K-Maps)
Next, we look for rectangles that are made entirely of 1s
  This K-map has 4 spots
  Does it have any rectangles of size 2? (e.g. 1x2 or 2x1)
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 17: Karnaugh Maps (K-Maps)
Next, we look for rectangles that are made entirely of 1s
  This K-map has 4 spots
  Does it have any rectangles of size 2? (e.g. 1x2 or 2x1) Yes
  Every rectangle can be represented by an expression
  What is the expression in this case?
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 18: Karnaugh Maps (K-Maps)
Next, we look for rectangles that are made entirely of 1s
  Both of these 1s represent different values for y
  … but they also both represent the same value of x
  In fact, the rectangle covers every situation where x = 1
  The expression, therefore, is x (x=0 would be x’)
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 19: Karnaugh Maps (K-Maps)
Next, we look for rectangles that are made entirely of 1s
  Since the rectangle we just found covers all of the 1s in the K-map, we are done
  The simplified expression is, therefore, f(x,y) = x
Note: Rectangles can, and often do, overlap
x | y | xy + xy’
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
0 | 1
0 | 1
x
y
0
1
0
1

## Slide 20: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Let’s fill in the K-map:
  g(a,b) = x + y
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 21: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Any rectangles of size 4?
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 22: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Any rectangles of size 4? No
  Any rectangles of size 2?
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 23: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Any rectangles of size 4? No
  Any rectangles of size 2? Yes
    What is the expression for this rectangle?
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 24: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Any rectangles of size 4? No
  Any rectangles of size 2? Yes
    What is the expression for this rectangle? x
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 25: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Any rectangles of size 4? No
  Any more rectangles of size 2?
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 26: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Any rectangles of size 4? No
  Any more rectangles of size 2? Yes
    What is the expression for this rectangle? y
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 27: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Any rectangles of size 4? No
  Any more rectangles of size 2? Yes
    What if just added a 1x1 rectangle, instead?
    This expression is x’y (this is not as much of an improvement)
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 28: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Are we done?
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 29: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Are we done? Yes, because all 1s have been covered by rectangles
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 30: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Are we done? Yes, because all 1s have been covered by rectangles
  Note: We could add another rectangle here, but that would be unnecessary since we have covered all 1s already
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 31: Karnaugh Maps (K-Maps)
Another example: g(a,b) = xy + x’y + xy’
  Are we done? Yes, because all 1s have been covered by rectangles
  Therefore, g(a,b) = x + y
x | y | xy + x’y + xy’
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 1
1 | 1
x
y
0
1
0
1

## Slide 32: Karnaugh Maps (K-Maps)
K-maps for 3 variables have a notational quirk:
x | y | z | xy + x’z + yz
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 33: Karnaugh Maps (K-Maps)
K-maps for 3 variables have a notational quirk:
x | y | z | xy + x’z + yz
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10
Note the unusual order, here:
Notes: Please note that 3-variables could be represented with a 3-dimensional shape, but this does not scale to 4 or more variables (at least not for us humans).

## Slide 34: Karnaugh Maps (K-Maps)
Let’s continue this example
  Are there any size 8 rectangles? (remember, the rectangles must be of size 2n)
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 35: Karnaugh Maps (K-Maps)
Let’s continue this example
  Are there any size 8 rectangles? No
  Are there any size 4 rectangles?
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 36: Karnaugh Maps (K-Maps)
Let’s continue this example
  Are there any size 8 rectangles? No
  Are there any size 4 rectangles? No
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 37: Karnaugh Maps (K-Maps)
Let’s continue this example
  Are there any size 8 rectangles? No
  Are there any size 4 rectangles? No
  Are there any size 2 rectangles?
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 38: Karnaugh Maps (K-Maps)
Let’s continue this example
  Are there any size 8 rectangles? No
  Are there any size 4 rectangles? No
  Are there any size 2 rectangles? Yes
    xy
    x’z
    yz
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 39: Karnaugh Maps (K-Maps)
Let’s continue this example
  Are there any size 8 rectangles? No
  Are there any size 4 rectangles? No
  Are there any size 2 rectangles? Yes
    xy
    x’z
    yz
    Right?
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 40: Karnaugh Maps (K-Maps)
Let’s continue this example
  Are there any size 8 rectangles? No
  Are there any size 4 rectangles? No
  Are there any size 2 rectangles? Yes
    xy
    x’z
    yz
    Right? No! The term yz is unnecessary
    h(x,y,z) = xy + x’z
0 | 0 | 1 | 0
1 | 1 | 1 | 0
xy
z
00
0
1
01
11
10

## Slide 41: Karnaugh Maps (K-Maps)
4-variable K-maps look like this:
  f(a,b,c,d) = abc’d’ + abc’d + abcd + abcd’ + a’bc’d + a’bcd + a’b’c’d + ab’c’d
Note: We will not do K-maps for any expressions beyond 4 variables
0 | 0 | 1 | 0
1 | 1 | 1 | 1
0 | 1 | 1 | 0
0 | 0 | 1 | 0
ab
cd
00
00
01
01
11
10
11
10
Notes: Let’s simplify this one, as another example

## Slide 42: Karnaugh Maps (K-Maps)
Truth tables can sometimes have don’t care conditions
When this happens, we can treat it as either a 0 or a 1
  Whichever is more convenient for finding our rectangles
In this example, the ? should be a 1 since it enables this 1x4 rectangle
0 | 0 | 1 | 0
1 | ? | 1 | 1
0 | 1 | 1 | 0
0 | 0 | 1 | 0
ab
cd
00
00
01
01
11
10
11
10

## Slide 43: Karnaugh Maps (K-Maps)
K-maps have one other confusing aspect for students
  The positions in this table are adjacent because the values next to each other (horizontally or vertically) differ by exactly one bit
  Notice that the left and right columns for 3 or 4-variable k-maps (and the top and bottom rows) also differ by exactly one bit
0 | 0 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 1 | 0
ab
cd
00
00
01
01
11
10
11
10
Notes: Let’s simplify this one, as another example

## Slide 44: Karnaugh Maps (K-Maps)
K-maps have one other confusing aspect for students
  As a consequence, these are valid rectangles:
0 | 0 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 1 | 0
ab
cd
00
00
01
01
11
10
11
10

## Slide 45: Karnaugh Maps (K-Maps)
00
K-maps have one other confusing aspect for students
  As a consequence, these are valid rectangles
  … and so is this:
0 | 0 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 1 | 0
cd
00
01
01
11
10
11
10
ab

## Slide 46: Common Components
CSCI 2050U - Computer Architecture

## Slide 47: Tri-state Buffer
A tri-state buffer is a component, much like a buffer, that does not change the value on the line
  However, it can block the value so that there is no value

## Slide 48: Decoders
A decoder (DEC) is a component which activates (i.e. voltage high, e.g. 5v) one of its output lines for each unique input combination
  Inputs: n
  Outputs: 2n

## Slide 49: Decoders
A decoder is a component which activates (i.e. voltage high, e.g. 5v) one of its output lines for each unique input combination
  This is a 2-to-4 line decoder
00
01
10
11

## Slide 50: Decoders
A decoder is often used for two important purposes:
  Decoding an instruction, enabling the correct ALU circuit
  Decoding a memory address, enabling the inputs and/or outputs of the correct memory cell

## Slide 51: Decoders
Decoders and other components can be drawn in block notation
  This abstraction simplifies our job as we move to more complex circuits
DEC

## Slide 52: Multiplexer
A multiplexer (MUX) is a component with many inputs and only one output
  This is a 4-to-1 multiplexer
  Selector bits (A and B in the diagram, below) decide which input gets mapped to the output
  Selector bits: n
  Input bits: 2n
output
input1
input2
input3
input4

## Slide 53: Multiplexer
The multiplexer in block notation:
output
input1
input2
input3
input4
MUX

## Slide 54: Half Adder
A half adder (HA) can add two bits together
  Inputs:
    A and B: The two bits to add
  Outputs:
    S: The sum of the two bits
    C: Carry (1 if there was a carry, 0 if not)

## Slide 55: Half Adder
A half adder can add two bits together
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 56: Half Adder
A half adder can add two bits together
  Recognize this truth table?
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 57: Half Adder
A half adder can add two bits together
  Recognize this truth table? S = A’B + AB’ = A ⊕ B
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 58: Half Adder
A half adder can add two bits together
  Recognize this truth table? C = AB
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 59: Half Adder
A half adder circuit:
  S = A’B + AB’ = A ⊕ B
  C = AB

## Slide 60: Half Adder
A half adder in block notation:
HA

## Slide 61: Full Adder
Why do they call it a half adder?
To find the answer to this, we need to try to add two multi-bit numbers
Let’s add 0001 and 0110:
0011
+0111

## Slide 62: Full Adder
Why do they call it a half adder?
To find the answer to this, we need to try to add two multi-bit numbers
Let’s add 0001 and 0110:
  Adding the rightmost two bits can be done with a half adder
1
0011
+0111
0

## Slide 63: Full Adder
Why do they call it a half adder?
To find the answer to this, we need to try to add two multi-bit numbers
Let’s add 0001 and 0110:
  Adding the rightmost two bits can be done with a half adder
  What about the next two bits?
1 1
0011
+0111
10

## Slide 64: Full Adder
Why do they call it a half adder?
To find the answer to this, we need to try to add two multi-bit numbers
Let’s add 0001 and 0110:
  Adding the rightmost two bits can be done with a half adder
  What about the next two bits?
    We really need to add three bits, in the general case
    For this we need a new component: the full adder (FA)
1 1
0011
+0111
10

## Slide 65: Full Adder
A full adder (FA) adds three bits
  Inputs:
    A and B: The bits to be added
    Cin: A carry from a previous add, which also must be added
  Outputs:
    S: The sum of the three bits
    Cout: Whether or not the sum resulted in a carry bit
HA
HA

## Slide 66: Full Adder
We could have drawn this entire circuit using XOR, AND, and OR gates
This is our first circuit, drawn using block notation
This is called a ripple carry adder

## Slide 67: Wrap-Up
Optimization
  Algebraic simplification
  Karnaugh maps
Common components