## Slide 1: x86-64 Assembly Language
CSCI 2050U - Computer Architecture
Randy J. Fortier
@randy_fortier

## Slide 2
Outline
Development tools
Registers
A basic program
Arithmetic instructions
Variables
Branching/jumping
Functions and the stack

## Slide 3: Development Tools
CSCI 2050U - Computer Architecture

## Slide 4
Language Translators
Interpreters translate each high-level language source code line every time it is needed for execution
  e.g. JVM, Python
Compilers translate HLL source code to object code that is almost ready for the CPU to execute
  e.g. C++
Assemblers translate assembly language – a low level language – to object code

## Slide 5
Linker
Object code files produced by a compiler or assembler are not quite ready for execution
A linker combines object code files and prepares them to be loaded into memory for execution

## Slide 6
Debugger
Allows the programmer to control execution of a program
  Step through instructions one at a time
  Stop at a preset breakpoint
Lets you look at memory or register contents
  Helps find programming errors
  Helps understand how the computer works

## Slide 7
Integrated Development Environments
Single interface provides access to text editor, compiler or assembler, linker, and debugger
IDEs for developing assembly language:
  Microsoft Visual Studio
  Code::Blocks
  Eclipse
  SASM

## Slide 8: Registers
CSCI 2050U - Computer Architecture

## Slide 9
RAX
General Purpose Registers
RAX, RBX, RCX, RDX, each 64 bits long (quadword)
EAX
AX
AH
AL
RBX
EBX
BX
BH
BL
… for RCX and RDX …
RCX
ECX
CX
CH
CL
RDX
EDX
DX
DH
DL

## Slide 10
R8
General Purpose Registers
These registers are new to x64 (64-bit)
R8D
R8W A
R8B
R9
R9D
R9W W
R9B
R10
R10D
R10W W
R10B
R11
R11D
R11W W
R11B
R12
R12D
R12W W
R12B
R13
R13D
R13W W
R13B
R14
R14D
R14W W
R14B
R15
R15D
R15W W
R15B

## Slide 11
Index Registers
RSI - source index
  Source address in string moves
  Array index
  General purposes
RDI - destination index
  Destination address in string moves
  Array index
  General purposes

## Slide 12
Floating Point Registers
XMM0 – XMM15 – 128-bit floating point registers
  Available in SSE-compatible processors
  Includes Pentium III and later
YMM0 – YMM15 – 256-bit floating point registers
  Available in AVX-compatible processors
  Includes Core, Core Duo, Core2 Duo, i3, i5, and i7
ZMM0 – ZMM31 – 512-bit floating point registers
  To be introduced in AVX512-compatible (Xeon) processors

## Slide 13
Stack Registers
RSP - stack pointer
  Holds address of top of stack frame
RBP - base pointer
  Used in procedure calls to hold address of reference point in the stack (i.e. bottom of stack frame)

## Slide 14
Other Registers
RIP - instruction pointer
  Holds address of next instruction to be fetched for execution
EFLAGS - flags
  Collection of flags, or status bits
  Records information about many operations
    Carry Flag (CF) is bit 0
    Zero Flag (ZF) is bit 6
    Sign Flag (SF) is bit 7
    Overflow Flag (OF) is bit 11

## Slide 15: A Basic Program
CSCI 2050U - Computer Architecture

## Slide 16
A Basic Assembly Program
section .data
message db "This is a message from Linux assembly!", 0ah, 0dh
section .text
global _start
; more system calls are provided in:
;http://blog.rchapman.org/posts/Linux_System_Call_Table_for_x86_64
_start:
mov rax, 1 ; syscall number for sys_write()
mov rdi, 1 ; standard output
mov rsi, message ; what to print
mov rdx, 40 ; how many characters to print
syscall
; exit
mov rax, 60 ; syscall number for sys_exit()
mov rdi, 0 ; exit code (0 means success)
syscall
comments
directives
comments
instructions

## Slide 17
Directives
Provide instructions to the assembler
Typically don’t cause code to be generated
Examples
  .section text - tells the assembler the where the instructions are to be found
  .section data - tells the assembler the where the data is to be found
  db - tells the assembler to reserve space for an 8-bit byte/character value

## Slide 18: Basic and Arithmetic Instructions
CSCI 2050U - Computer Architecture

## Slide 19
Basic Instructions
Each corresponds to a single instruction actually executed by the CPU
Examples
mov rax, number
  copies a quadword from memory to the register RAX (also called the accumulator)
add rax, 24
  adds the quadword representation of 24 to the number already in RAX, replacing the number in RAX
sub rax, 24
  subtracts the quadword representation of 24 from the number already in RAX, replacing the number in RAX

## Slide 20
Parts of an Instruction
Instruction’s object code begins with the opcode, usually one byte
  Example, A1 for mov rax, number
Immediate operands are constants embedded in the object code
  Example, 0000009E for add rax, 158
Addresses are assembly-time; must be fixed when program is linked and loaded
  Example, 00000004 for mov sum, rax

## Slide 21
Types of Instruction Operands
Immediate mode
  Constant assembled into the instruction
Register mode
  A code for a register is assembled into the instruction
Memory references
  Several different modes

## Slide 22
Memory References
Direct – at a memory location whose address is built into the instruction
  Usually recognized by a data segment label
  e.g., mov sum, rax
    (here rax is a register operand)
Register indirect – at a memory location whose address is in a register
  Usually recognized by a register name in brackets,
  e.g., mov qword [rbx], 10
    (here 10 is an immediate operand)

## Slide 23
Memory References - Examples
[rbp] - base register only
[rbx + rdi * 4] - base + index * scale
[rbp + rax] - scale is 1 (bytes)
[rax - 8] – offset by -8
[rax + rdi * 8 + 4] - all four components
[rax + offset] - uses the address of the variable 'offset' as the offset
...more...

## Slide 24
Multiplication – MUL and IMUL
Multiplication is different for unsigned (MUL) and signed (IMUL) numbers
  e.g. mul 2
    Of course, the operand can be memory or a register, as well
    The second operand is implicit:
Size | 2nd operand | Result
byte | AL | AX
word | AX | DX:AX
dword | EAX | EDX:EAX
qword | RAX | RDX:RAX

## Slide 25
Division – DIV and IDIV
Division is different for unsigned (DIV) and signed (IDIV) numbers
  e.g. div 2
    Of course, the operand can be memory or a register, as well
    The second operand is implicit:
Size | 2nd operand | Quotient | Remainder
byte | AX | AL | AH
word | DX:AX | AX | DX
dword | EDX:EAX | EAX | EDX
qword | RDX:RAX | RAX | RDX

## Slide 26
Shifting
Move all bits left (or right) 3 positions:
  shl rax, 3 (or shr rax, 3)
Move all bits left (or right) 3 positions (sign is preserved) (arithmetic shift):
  sal rax, 3 (or sar rax, 3)
There are also rotations
  Instead of dropping the bit on the left (or right), it is wrapped around
  rol rax, 3 (or ror rax, 3)

## Slide 27: Variables
CSCI 2050U - Computer Architecture

## Slide 28
Variables
Variables are often declared in their own sections of the program
  .data – initialized data
  .bss – uninitialized data
  .rodata – read only (initialized) data
Variables can also be:
  Stored on the calling stack (i.e. local variables)
  Allocated on the heap (e.g. with malloc())

## Slide 29
Variables
Assembly language does not have types
  e.g. If you want a number to be signed, you need to initialize it properly, and use instructions intended for signed numbers
It does support sizes, however
  db – byte (8-bit)
  dw – word (16-bit)
  dd – double word (32-bit)
  dq – quad word (64-bit)
  do – octo word (128-bit)

## Slide 30
Variables – Some Examples
section .data
string1: db "What's your name? ", 0
string2: db "a", "b", "c", 0
number: dq 0
array1: dq 0, 1, 2, 3, 4, 5
array2: times 10 dq 0
section .bss
command: resb 100
array3: resq 10

## Slide 31: Branching and Jumping
CSCI 2050U - Computer Architecture

## Slide 32
Branching/Jumping
Branching (also called jumping) is when program flow does not simply flow to the next instruction
A branch instruction may modify the RIP register
Unconditional jumping
  Always set the RIP register to the specified address
  Basically, a GOTO statement
Conditional jumping
  Jump only when some condition is true

## Slide 33
Comparisons
The cmp instruction is similar to a subtract, except that it doesn't modify its operands
  Only the flags are modified

## Slide 34
Flags
Flag | Meaning
Z (Zero) | Set when the result of an arithmetic operation is zero
O (Overflow) | Set when an arithmetic operation resulted in overflow
S (Sign) | Set when an arithmetic operation resulted in a negative result
C (Carry) | Set when an arithmetic operation resulted in carry

## Slide 35
Conditional Jump Instructions
These instructions jump when certain flags are set (or are not set)
  Often by a cmp instruction
Intuition | Unsigned | Signed
== | je | je
!= | jne | jne
< | jb | jl
≤ | jbe | jle
> | ja | jg
≥ | jae | jge

## Slide 36
Conditional Jump Instructions
These instructions jump when certain flags are set in other ways:
Instruction | Flags
jz | Z=1
jnz | Z=0
jc | C=1
jnc | C=0
jo | O=1
jno | O=0
js | S=1
jns | S=0

## Slide 37
Conditional Jump Instructions
These instructions jump depending on the value of the rcx, (ecx, …) register
  This register is often used as a loop counter
Instruction | Flags
jcxz | RCX==0
jcxnz | RCX!=0

## Slide 38
Implementing Conditionals
Conditional jumps make it easy to implement if/elseif/else statements
C++ | Assembly
int num = …; if (num < 10) { // do something } // the rest of the code | mov rax, [num] cmp rax, 10 jge skipCond ; do something skipCond: ; the rest of the code

## Slide 39
Implementing Loops
Conditional jumps also make it easy to implement while, do/while, and for loops
C++ | Assembly
int num = …; while (num < 10) { // do something num++; } // the rest of the code | mov rax, [num] loopStart: cmp rax, 10 jge loopExit ; do something inc rax jmp loopStart loopExit: ; the rest of the code

## Slide 40: The Stack and Functions
CSCI 2050U - Computer Architecture

## Slide 41
Stack Instructions
These instructions are the most basic way to use the stack
  push rax – puts the value of rax onto the top of the stack
    rsp is decreased by the size of rax (8)
    rsp points to the top of the stack
  pop rax – pops the top of the stack into rax
    rsp is increased by the size of rax (8)
Note: The stack in x64 (and x86) grows downward
  i.e. the stack grows toward lower addresses, not higher addresses

## Slide 42
The Calling Stack
Every program has a dedicated program stack
Each time a function is called:
  Some arguments may be passed via registers
  Other arguments may be pushed onto the stack
    These arguments are pushed in reverse order
  The return address (rip) is saved onto the stack
  The stack base pointer (rbp) is saved onto the stack

## Slide 43
Passing Arguments as Registers
System V AMD64 ABI (application binary interface):
  A calling convention used by Linux, MacOS, BSD
  For integer or pointer arguments:
    rdi - first integer/pointer argument
    rsi - second integer/pointer argument
    rdx - third integer/pointer argument
    rcx - fourth integer/pointer argument
    r8 - fifth integer/pointer argument
    r9 - sixth integer/pointer argument
  All remaining arguments are passed via the stack
https://web.archive.org/web/20160801075139/http://www.x86-64.org/documentation/abi.pdf

## Slide 44
Passing Arguments as Registers
System V AMD64 ABI:
  For floating point arguments:
    xmm0 - first floating point argument
    xmm1 - second floating point argument
    xmm2 - third floating point argument
    xmm3 - fourth floating point argument
    xmm4 - fifth floating point argument
    xmm5 - sixth floating point argument
    xmm6 - seventh floating point argument
    xmm7 - eighth floating point argument
  All remaining arguments are passed via the stack
https://web.archive.org/web/20160801075139/http://www.x86-64.org/documentation/abi.pdf

## Slide 45
Passing Arguments on the Stack
System V AMD64 ABI:
  Recall that rsp points to the top of the stack
  When calling a function
    [rsp] contains the return address
    [rsp+8] contains the first stack parameter
https://web.archive.org/web/20160801075139/http://www.x86-64.org/documentation/abi.pdf

## Slide 46
Passing Arguments as Registers
System V AMD64 ABI:
  This ABI has one quirk
  rsp must be 16-byte aligned before making a call
    The process of making a call pushes the return address (8 bytes) on the stack
    If the size of the return address (8) + your stack arguments is not a multiple of 16, make that extra space yourself
      Push some placeholder values
      Subtract from rsp
https://web.archive.org/web/20160801075139/http://www.x86-64.org/documentation/abi.pdf

## Slide 47
Return Values
System V AMD64 ABI:
  Integers are returned in rax or rdx:rax, and floating point values are returned in xmm0 or xmm1:xmm0

## Slide 48
Passing Arguments as Registers
__fastcall ABI:
  A calling convention used by 64-bit Windows
    Integer arguments (and pointers) are passed in registers rcx, rdx, r8, and r9
    Floating point arguments are passed in xmm0l, xmm1l, xmm2l, and xmm3l
    16-byte arguments are passed by reference
    rax, r10, r11, xmm4, and xmm5 are considered volatile
    All other registers are non-volatile
    Return values are handled the same way as System V AMD64 ABI

## Slide 49
The Calling Stack
long func1(long a1, long a2, long a3, long a4,
long a5, long a6, long a7, long a8) {
long v1, v2;
...
}
stack
growth

## Slide 50
high
addresses
low
addresses
a8
a7
rip
rbp
v1
v2
a1
a2
a3
a4
a5
a6
rdi
rsi
rdx
rcx
r8
r9
The Calling Stack

## Slide 51
Returning from a Function
A function returns using the ret instruction
  ret pops rbp and rip off the stack, and resumes execution at rip+(instruction_size)
  If there are still local variables on the stack, these should be popped off
    If you do not, your program will almost certainly crash
  If there are still arguments on the stack, you can't pop them off
    The rbp and rip values are in the way

## Slide 52
Cleaning up the Stack
A function returns using the ret instruction
  If there are still arguments on the stack, you can't pop them off
    The rbp and rip values are in the way
  There is a version of ret that takes an integer operand
    The number of bytes to pop off the stack after popping rbp, rip
    e.g. ret 8 (pop 1 64-bit value off the stack)
  Alternatively, the caller of the function could pop the values off the stack after the function returns

## Slide 53
Wrap-up
In this section, we learned about:
Tools for writing assembly language programs
Registers
The structure of assembly language programs
Basic and arithmetic instructions
Declaring and storing data
Branching/jumping
Stack operations
Calling and declaring functions